Market

Municipal Drinking Water

Challenge

The challenge was to stop water leaking at the joints of a newly installed ductile iron pipe. The 30 & 36 inch ductile iron pipe had been cement lined and water was leaking in through the cement lining at the joints.

Engineered Solution     
To eliminate leaking joints, the HydraTite® Internal Joint Seal was proposed as a solution. The HydraTite® seal is a mechanical trenchless remediation for the joints that preserves the new ductile iron pipe.

Scope

Surface prep included chipping out the cement at the joints prior to installation of the HydraTite® seals. After approval of the repair by the client, the HydraTite® seals were manufactured and installed.

Solution

Once surface prep was completed, nineteen seals were installed. The HydraTite® seals eliminated the infiltration of the water at the joints. Rapid installation including the surface prep had the entire job completed within four days.

HydraTech Engineered Products, LLC

HydraTech Field Services, LLC
10448 Chester Road Cincinnati, Ohio 45215      Phone: (513) 827-9169      Fax: (513) 8279171

https://hydratechllc.com

https://hydratechllc.com/services/field-services/