Market:

Municipal / County

Challenge:

The challenge was to repair deteriorated timber support posts for several pavilions in lieu of replacing the entire support column.

Engineered Solution:

The solution utilized the HydraWrap® Structural Composite Repair System.

Scope:

The client was seeking an alternate solution to repairing timber support posts for park shelters. The support posts had deteriorated at the soil-to-air interface – where the support posts had been embedded in the concrete slab of the pavilion at the time of construction. The remainder of the timber support posts above the concrete slab was in good condition.

Solution:

To avoid replacing all of the support post, the client utilized the HydraWrap® carbon fiber system to restore the deteriorated sections of the timber posts at and below the concrete slab grade. The concrete slab, which had been included in the scope to be replaced, was removed to expose the embedded timberpost. The HydraWrap® system was used to restore the profile of the 6” X 6” timber post and provide a reinforced protective repair to prevent future deterioration.

HydraTech Engineered Products, LLC

HydraTech Field Services, LLC

10448 Chester Road, Cincinnati, Ohio 45215    Phone: (513) 827-9169    Fax: (513) 827-9171 http://www.hydratechllc.com

https://www.hydratechfs.com