Market:

Stormwater

Challenge:

MnDOT discovered two drainage pipes that needed rehabilitation. Both pipes had two joints of concern, one had a diameter of 48” and the other had a diameter of 72”. A trenchless option was preferred.

Engineered Solution:

HydraTite Internal Pipe Joint Seals were the selected repair method to avoid excavation.

Scope:

Mud was cleared away from the joints to ensure the seals could seal properly against the interior surface of the pipe. Extra-wide rubber seals were positioned over the joints in the 72” pipe and standard-wide rubber seals were installed over the joints in the 48” pipe. Two retaining bands were positioned into the rubber seals’ designated channels. These bands were expanded utilizing a hydraulic expander and locked in place with wedges. The project was completed in a few days with a crew of only two people.

Solution:

These two pipes were rehabilitated quickly using a solution that will last a lifetime. These four HydraTite seals fortified these joints against leaks.

HydraTech Engineered Products, LLC

HydraTech Field Services, LLC

10448 Chester Road, Cincinnati, Ohio 45215    Phone: (513) 827-9169    Fax: (513) 827-9171 http://www.hydratechllc.com

https://hydratechllc.com/services/field-services/